## Slide 1: 1.264 Lecture 36
Telecom: Wireless networks
Please do subject evaluation online
Notes: <number>

## Slide 2: Exercise
Design a system for an intercity rail passenger train to provide Internet access to its passengers and operating crew. Address each challenge:
  Metro areas: frequent physical obstructions, such as underpasses, tall buildings
  Tunnels
  Rural areas: gaps in cellular coverage, trees, hills obstruct line of sight
  Multiple applications: what to do when a user wants to download a 200MB file
  Network changes: train goes through many networks of varying quality at varying speeds
  Reception in passenger cars: metal car bodies affect signal
Notes: <number>

## Slide 3: Exercise
Rail line
Station
Tunnel
Buildings
Underpass
Rural
area
Hills, trees
Notes: <number>

## Slide 4: Solution
Metro area:
  Multiple cellular data carriers
  Server on train chooses best signal, maintains continuity
  Use WiFi (wireless LAN) at stations
Tunnels (short ones):
  Server on train caches Web content, handles email via store and forward
  Long tunnels require leaky fiber and/or base stations
Rural areas:
  Multiple cellular data carriers, and satellite services
Within train:
  Antennas mounted on multiple cars, wireless LAN between cars so any antenna can serve all cars
Server, applications:
  On train server manages traffic, ensures ‘fairness’
  Server handles authentication and billing
(How do long distance trucking, buses do this?)
Notes: <number>

## Slide 5: Solution example
www.pointshotwireless.com
Notes: <number>

## Slide 6: Solution example: Amtrak wireless coverage
Source: Amtrak
Notes: <number>

## Slide 7: Radio propagation
Losses:
  Free space loss
  Atmospheric attenuation: rain, water, dust
  Multipath loss: water body or fog causes reflections, and signals arrive out of phase at destination
  Diffraction: hills, buildings, obstructions
Antenna problems:
  Snow, icing (use heaters, radomes)
  Zoning restrictions (hide antennas in buildings)
Microwave frequencies are line of sight
  Behave like light, can be focused and reflected
These issues hold for mobile phones, wireless data, satellites also
Notes: <number>

## Slide 8: Radio loss
Notes: <number>

## Slide 9: Wireless LAN
Wireless LAN (WiFi) standard is IEEE 802.11
Two types of wireless LAN:
  Ad hoc, where stations (computers) directly connect
  Infrastructure, with an access point (AP) that connects to a wired LAN and usually a MAN/WAN
Distributed coordination required between stations due to collisions
  Carrier sense multiple access/collision avoidance (CSMA/CA) protocol is used, as discussed earlier
Wireless environment is very noisy
  Frames are fragmented into small frames so retransmission, which is frequent, is more efficient

## Slide 10: Wireless LAN service sets
A room or area is a typical BSS (basic service set)
An ESS is a set of rooms and areas in the LAN
Stations capabilities may be:
  Stationary only
  Can move within a single BSS (ad hoc or infrastructure)
  Can move between BSS, but communication may not be continuous during the move
From Forouzan

## Slide 11: Wireless LAN issues
WiFi (802.11b, 802.11g, 802.11n)
  Inexpensive, pervasive, reliable, easy to manage
  Hot spots common, but unscalable for metro area use
  Range ~100 meters: ok within buildings, campuses
  Bandwidth: 11 Mbps (b), 54 Mbps (g), 100 Mbps (n)
  Actual bandwidth often half of nominal due to interference, fading, etc.
  Half of traffic at many companies is non-work (music or video streaming, Web access, personal email, …)
  Security is difficult, because signals propagate beyond the building or site
    WEP easy to break; use WPA and WPA2 instead
    Don’t use WPS (WiFi protected setup); it has a security flaw
  Municipal network plans problematic (30+ points/sq mi)
Notes: <number>

## Slide 12: Exercise
In a warehouse, what type of LAN would you set up (ad hoc, BSS, ESS), and why?
  Assume there are forklifts and other vehicles operating
  Assume there are pick/pack stations, conveyors, etc.
Would you try to lay out the network to minimize handoffs, or is that not important? Why or why not?
With 802.11b, how would you stream video from 25 forklifts/vehicles in the warehouse?
  Assume your video is 1.5 Mbps

## Slide 13: Solution
Set up an ESS, to allow handoffs and to connect all devices/stations to the WAN if needed
Lay out the network to cover aisles/areas that minimize handoffs
  Communications is not continuous in wireless LAN handoffs
Video: 802.11b is 11 Mbps, or 5.5 Mbps practically
  You need 25 * 1.5 Mbps, or 37.5 Mbps, or at least 8 BSS, which is one AP for every 3 vehicles in an area
  Because of interference, fading, etc. you may need more
  If you use 802.11n, at 100 Mbps nominal or 50 Mbps actual, you may find 2 APs sufficient (1 for redundancy)

## Slide 14: Mobile telephony
Mobile telephony is dominant. Alternatives are:
  Specialized mobile radio (SMR), used primarily for local dispatch
    About 3,000 licensed SMR providers in US (taxi, trucking..)
    Nextel bought many SMR providers and created national network: radio, cell phone, data, messaging
    Nextel uses variation on GSM cellular technology
  Private mobile radio service (police, fire, railroads…)
    Shared frequencies among all users
    Base stations, repeaters; squelch or tone control
    Trunking radio (multiple channels) used by larger organizations
      One control channel to which all units listen
      Talk channel then designated
  These options use spectrum less well than cell phones
    Being pushed to narrowband; other measures
Notes: <number>

## Slide 15: Mobile (cellular) telephony
A cell phone is a radio
Before cell phones, there was mobile radio, with one tower per metro area and about 25 channels
  Car phones had to be high powered but for little usage
Cellular telephony divides a metro area into cells for much, much more capacity
832 channels in standard US cellular radio spectrum band; European GSM varies but similar
  Up to 5 more bands have been allocated via auction in US
  Phone can operate on any of these 1,000+ channels
Cellular switches are called Mobile Telephone Switching Offices, or MTSOs
  Functions same as standard telco voice switch, plus handoff across cells, for voice calls
  Handles TCP/IP data for data and video
Notes: <number>

## Slide 16: GSM (2G)
GSM is European standard, adopted worldwide and increasingly in US
  It’s a 2G (second generation) standard, being superseded by 3G
  It switches voice calls, like landlines, and is being replaced by voice over IP
Each voice band is 13 kbps (versus 64 kbps fiber)
Standard GSM has 124 channels
Each channel is 270.8 kbps carried in 200 kHz
  8 users per channel
  GSM can (re)use 1/3 of channels in each cell, due to good error correction
  Capacity =~ 124 channels * 8 users/channel * 1/3 reuse= 329 calls (users) per cell
GSM data is carried over GPRS (General Packet Radio Services), often considered 2.5G

## Slide 17: 3G wireless
Worldwide standard, though frequency bands vary by region
  Roaming phones must use different frequency bands
  There are a few common frequency bands worldwide
Designed for many services:
  Real-time gaming
  Voice
  File download and upload
  Video
  Web and email
3G data protocols are WCDMA, HSPA
  In broad use, continue to evolve new features
  Will be supported for many years until full 4G usage
  Data rates of 500 kbps to 1 Mbps typical

## Slide 18: 4G wireless
4G is also called LTE (long term evolution) and release 8.
  Standard is 3GPP (in GSM lineage)
  Not backward compatible with 3G
  Entirely IP based; no voice switched traffic
  Supports spectrum flexibility for worldwide operation
  Handoffs at 350 km/hr to support high speed rail
  (Any individual phone supports limited spectrum, since RF and filter design are expensive/inflexible)
  Data rates of up to 20 Mbps typical
  Scarcity of bandwidth resulting in throttling of use
CDMA (50% of US) 1x-EV-DO Rev C is very similar to LTE, and is converging.
  Standard is 3GPP2 (in CDMA lineage)

## Slide 19: Frequency reuse in cellular telephony
This is a 7-cell pattern; 9-cell is also common.
Notes: <number>

## Slide 20: Cellular serving plan
Simple honeycomb pattern rarely holds. Actual cell coverage highly variable.
Notes: <number>

## Slide 21: Exercise
Assume LTE can provide 20 Mbps to areas with industry/warehousing to each location served
  Assume 100 locations in the cell
  Assume each has 10 Web users (1 Mbps), 1 Web/data server (5 Mbps), limited videoconference/video (4 Mbps)
    Total bandwidth for each location is 10 Mbps (1+5+4)
Compare LTE to:
  DSL (1.5-13 Mbps, asymmetric)
  CATV (30-300 Mbps, asymmetric but shared over all 100 users
  T1 over copper (1.5 Mbps, symmetric)
  Gigabit Ethernet MAN (1 Gbps, symmetric)
Can LTE solve the ‘last mile’ problem sometimes?

## Slide 22: Solution
An average user needs 10 Mbps
  DSL (1.5-13 Mbps) may meet it in some cases, but usually not. DSL usually 3-6 Mbps
  CATV has 30-300 Mbps, but 100 users *10 Mbps= 1 Gbps. CATV would need many segments; not effective.
  T1 over copper (1.5 Mbps) is not enough
  Gigabit Ethernet MAN is plenty, of course
  LTE (20 Mbps) is sufficient if bandwidth is available. In lower and medium density areas, it should be ok.
    A cell can handle 100+ channels at 20 Mbps
  LTE appears to solve the ‘last mile’ problem for residences (low/medium density) and low/medium density small business, but not major bandwidth users

## Slide 23: Long-range wireless: satellite communications
Notes: <number>

## Slide 24: Satellites (wireless WAN)
GEO satellites are on the equator and orbit every 24 hours, appearing stationary
  3 satellites 120 degrees apart can cover the Earth
MEO orbits are between the two Van Allen belts of charged particles that would destroy a satellite
  MEO satellites orbit every 6 to 8 hours
  GPS is a set of 24 MEO satellites in 6 orbits, designed so 4 satellites are always visible from any point on Earth
  GPS triangulates among the 4 satellites to determine position in 3D; it computes intersection of spheres
LEO satellites are in polar orbits
  They orbit every 90 to 120 minutes
  They are managed like a set of cells on Earth
  “Little” LEOs: text messaging (e.g. trucking)
  “Big” LEOs: Iridium, Globalstar (e.g. sat phones)
  Broadband LEOs: network video, other broadband

## Slide 25: GEO satellite applications
Inmarsat for marine and remote applications
  300,000 ships, vehicles, aircraft
  432 kbps Internet access data rate, 11 satellites
  Morse service ended in 2005 for commercial vessels
Very small aperture terminal (VSAT): 56 kbps- 4 Mbps for remote areas.
  Some areas can get 18 Mbps down, 4 Mbps up
  Most data rates 512 kbps or less down, 128 kbps up
  ‘Satellite Internet providers’ for rural consumers
  VSAT operators for Africa, other areas without fiber
TV programming distribution
Direct broadcast TV
Notes: <number>

## Slide 26: MEO, LEO satellite applications
Broadband LEO:
  Teldesic, similar to fiber, failed
Big LEO:
  Iridium not successful but still operating
    Too expensive to compete with terrestrial cell service
    66 satellites, each with 48 spot beams: ~2000 cells
    Voice, fax, paging at 2.4 to 4.8 kbps
  Globalstar has 48 satellites, similar service as Iridium
Little LEO:
  Trucking and rail information systems, paging
MEO:
  Global positioning system (GPS)
Notes: <number>

## Slide 27: Satellite links
Notes: <number>

## Slide 28: Satellite data
Delay:
  250 milliseconds (1/4 second) delay between two Earth stations communicating via geosynchronous (GEO) satellite
  Delay noticeable for voice communications
  Delay requires special treatment of data
    TCP/IP will assume network congestion or dropped packets with these delays; must use special parameters or equipment to spoof acknowledgements
Rain absorption
Sun transit outage at equinoxes
Power is limited on satellite
  Limited signal to noise ratio, limits bandwidth
  Direct Broadcast Satellite (DBS) satellites are overpowered to allow small consumer antennas; overall system costs are high
Little room left for satellites in equatorial (GEO) orbit
Notes: <number>

## Slide 29: Exercise
You operate a diamond mine in northern Canada and need 20 Mbps to remotely monitor and diagnose mining equipment, provide Internet and some video for employees, handle email and files, etc.
  Compare GEO, big LEO, little LEO, broadband LEO, MEO to meet your needs
  Where would the other end of the satellite link connect? Does it matter? Options are your corporate HQ, a large peering point, etc.

## Slide 30: Solution
If you need 20 Mbps up and down in northern Canada:
  GEO offers max 18 Mbps down and 4 Mbps up, and not in all areas.
  Polar areas are strange: beams are turned off from lack of demand but could possibly be turned on
  You might need 5 connections, which would be expensive…but a diamond mine can probably pay it
  Big LEO and Little LEO are low bandwidth
  MEO does not offer data services
  Broadband LEO (Teledesic) failed
Probably connect near corporate HQ to use MAN from ground station to HQ for cost, bandwidth, security reasons

## Slide 31: Glossary
BSS: Basic service set (WiFi)
ESS: Extended service set (WiFi)
WEP: Wired Equivalent Privacy (WiFi security)
WPA: WiFi Protected Access (WiFi security)
SMR: Specialized Mobile Radio
CDMA: Code Division Multiple Access (US wireless)
GSM: Global System for Mobile Communications (wireless voice standard, worldwide)
GPRS: General Packet Radio Service, over GSM
WCDMA: Wideband Code Division Multiple Access (3G data standard)
HSPA: High Speed Packet Access (3G data std)
3GPP: 3G Partnership Project (sets 3G/4G stds)
1x EV-DO: Evolution-Data Optimized (3G CDMA std)