## Slide 1: 1.264 Lecture 32
Telecom: Basic technology
Next class: Green chapter 4, 6, 7, 10. Exercise due before class
Notes: <number>

## Slide 2: Exercise 1
Communications at warehouse
  A warehouse scans its inventory with RFID readers that read every item every 15 minutes. There are 100,000 items in inventory. The sweep takes one minute to complete, so the data is bursty. The data is sent to the data center 3 km away as it is read. Each RFID tag transmits 256 bits of information, and is read four times per sweep (either by different readers or multiple times by the same reader). TCP/IP and HTTP headers double the size of the data.
  What is the total bandwidth required?
  Would 10 Mbps Ethernet work?
  Would 100 Mbps Ethernet work?
  Would cellular 500 kbps link work?
  Maximum Ethernet copper cable length is 100 meters.
    How would you connect points 3 kilometers apart if you have right of way?
    Don’t have right of way?
Notes: <number>

## Slide 3: Solution
Communications at warehouse
  What is the bandwidth required?
    100 000 x 4 x 256 bits / 60 sec x 2 ~= 3.4 Mbps
  Would 10 Mbps Ethernet LAN work?
    Yes
  Would 100 Mbps Ethernet LAN work?
    Yes
  Would cellular 500 kbps link work?
    No. Bandwidth too low.
    Unless you send data over 15 minutes, which is possible if you store it and/or process it (with a server) at warehouse
    This is a typical business/ops decision affected by telecom
  The maximum Ethernet copper cable length is 100 meters. How would you connect points 3 kilometers apart?
    If you have right of way: use fiber adapter and fiber optic cable
    If you don’t have right of way: obtain carrier Ethernet service
    Or use 4G wireless, if available, but it’s often more expensive
Notes: <number>

## Slide 4: Exercise 2
Why do we bother with wired telecommunications?
  Why not use wireless everywhere?
Why do companies design and manage their own networks?
  Local area network
  Wide area network
When do companies build their own network, versus lease facilities, versus buy carrier solution? Why?
For each these companies, indicate whether they probably build their own, lease facilities or buy a carrier solution, and briefly explain why:
  MBTA, UPRR, MITFCU, Bertucci, Citibank, NBC, AA
Notes: <number>

## Slide 5: Solution
Why do we bother with wired telecommunications?
  Bandwidth hugely greater; reliability, latency much better
Why do companies design and manage their own networks?
  Local area network: Inexpensive, easy, no exotic skills reqd
  Wide area network: Security, control, quality of service
When do companies build their own network, versus lease facilities, versus buy carrier solution?
  MBTA: Builds own. Has row, hard to manage
  UPRR: Builds own. Has row, easy to manage
  MITFCU: Carrier: Small, lease expensive, no row
  Bertucci: Carrier: Small, lease expensive, no row
  Citibank: Lease: Large, manage own facilities, no row
  NBC: Lease + satellite: Large, manage own net, no row
  AA: Lease: Large, manage own facilities, no row
Notes: <number>

## Slide 6
Telecom can enable supply chain innovation
Supply chain analyzes time, space, things, people. Consolidation is a key
tool in improving supply chain. Telecom allows location flexibility.
Notes: <number>

## Slide 7: Telecom equipment is reliable
99.9%: “ 3 9s”
  Downtime 9 hours per year (rounded to 10)
  Typical of older or unmanaged wired local area nets (LANs), and wireless wide area nets (WANs- 2G data)
99.99%: “ 4 9s”
  Downtime of 0.9 hours per year (rounded to 1)
  Typical of modern, managed, wired LANs and WANs, and wireless LANs
99.999%: “ 5 9s”
  Downtime of 0.09 hours per year (rounded to 5 minutes)
  Typical of individual telecom switches, routers, fiber links
    Downtime often 1 minute or less per year
And downtime is expensive:
  $200,000/hr for Amazon, $6 million/hr for brokerage
Notes: <number>

## Slide 8: Telecom in business
Open Internet is not generally usable for business:
  Limited or no service level guarantees: “best effort”
  Security is difficult
    Exposes your servers to criminal organizations
Businesses use or build their own networks using Internet standards
  Private networks, using leased lines
  Shared business networks provided by carriers
    Physical security and/or encryption
    Isolated from open Internet
  Encrypted “tunnels” over Internet if necessary
  Consumer contact via open Internet, of necessity
  Wireless connectivity is open, of necessity
Notes: <number>

## Slide 9: Data communications
Elements: sender, receiver, message, transmission medium, protocol (rules/process)
Data representation: data (text, numbers/binary, images), voice, video
Data flow: simplex (one-way), duplex (two-way)
Network type: local (LAN), wide-area (WAN), metro area (MAN), interconnected as Internet
  LAN, MAN, WAN serve different distances
Addressing: Ethernet, IP, port, URL, email, …
Standards: ISO, ITU-T, ANSI, IEEE, EIA, Internet
Notes: <number>

## Slide 10: Analog bandwidth
Analog bandwidth= (highest – lowest) frequency of signal. Hz= 1 cycle/second
  Voice telephony: 300 Hz- 3300 Hz or 3000 Hz or 3 kHz
  AM radio: 10 kHz bands. 950 AM is 945 kHz to 955 kHz
  FM radio: 200 kHz bands. 95.3 is 95.2 MHz to 95.4 MHz
  Analog black-and-white TV: 6 MHz bands
    TV is 525 by 700 lines, or 367,500 pixels
    Scan 30 times/second: send 30*367,500, or 11 Mpixels/sec
    Send 2 pixels/cycle: min amplitude for 1 color, max for other
    Need ½ *11 Mpixels/sec, or 5.5 MHz= 5,500,000 cycles/sec
    Alternating pixels is worst case; can send color in 6MHz too, with sophisticated coding
Notes: <number>

## Slide 11: Digital bandwidth
Digital bandwidth= bits per second. Examples:
  Text at 100 pages/second: 24 lines * 80 columns * 8 bits/character * 100= 1,536,000 bps= 1.5 Mbps
  Digitized voice: 4000 Hz * 2 samples/Hz * 8 bits= 64 kbps
  HDTV: 1920 * 1080 pixels * 30 frames/second *24 bit (each color pixel)= 1,492,992,000 bps= 1.5 Gbps
    Reduced to 20 to 40 Mbps by compression (factor of 38-75)
Digital signals carried over analog links
  Digital bandwidth~= analog bandwidth *SNR/3
    Where SNR= signal/noise power ratio in decibels (base 10)
      SNR= 10 log10(signal power/noise power)
  Phone line: 3000 Hz, SNR= 35
    Digital capacity= 3000 * 35/3= 35,000 bps
    This is capacity of dialup modem upstream
    Tweaks are used to get 56,000 bps downstream
Notes: <number>

## Slide 12: Exercise 3: Bandwidth
A wireless LAN has analog bandwidth=2 MHz and SNR= 30. Compute the digital bandwidth (Mbps)
This LAN must connect 9 devices, each transmitting to the LAN access point at 2 Mbps.
  The LAN should operate at 70% capacity or less
  Is the LAN capacity sufficient?
If the SNR is raised to 36, what is the digital bandwidth? Is this sufficient?
  This can be done by increasing signal strength or lowering the noise

## Slide 13: Solution
A wireless LAN has analog bandwidth=2 MHz and SNR= 30. Compute the digital bandwidth (Mbps)
  20 Mbps= 2 MHz * 30/3
This LAN must connect 9 devices, each transmitting to the LAN access point at 2 Mbps.
  The LAN should operate at 70% capacity or less
  Is the LAN capacity sufficient?
  Capacity required= 9 * 2= 18 Mbps
  Practical capacity= 20 Mbps*0.7= 14 Mbps. Not sufficient
If the SNR is raised to 36, what is the digital bandwidth?
  At SNR=36, digital bandwidth= 24 Mbps= 2 MHz*36/3
  Practical capacity= 24 Mbps*0.7= 16.8 Mbps. Almost ok.

## Slide 14: Transmission: Frequency division multiplexing (FDM)
FDM is traditional method of carrying multiple channels on a cable
Similar to radio broadcasting with stations at different frequencies
Used in DSL, CATV, satellite, cell phones…
Basic frequency is 4kHz band, based on voice needs
Ear hears (voice) from 20 to 20,000 Hz, but mostly 300 to 3500 Hz
Notes: <number>

## Slide 15: Transmission: Time division multiplexing (TDM)
Time division multiplexing (TDM) samples each 4kHz channel
Nyquist’s theorem: Sample at twice the bandwidth to code and decode all
possible information
So, sample 8000 times/second at 8 bits per second (or 256 levels)
Yields 64kb/sec channel, which is the basic rate of voice and data comm
24 64kb/sec channels is a T-1 (32 64 kb/sec channels in Europe form an E-1)
TDM used in fiber optic technologies; lasers can do both TDM and FDM (colors)
Notes: <number>

## Slide 16: Transmission: T-1 (copper or fiber)
8,000 samples per second
x 8 bits per sample
64,000 bits per channel
x 24 channels
1,536,000 bits per second
+ 8,000 framing bits per second (not enough!)
1,544,000 bits per second total in T-1 circuit
Framing used to keep sync between ends of circuit. If all 24 circuits are quiet, only framing bits keep the clocks at both ends of the circuit in sync (several framing systems used)
T-1 is often the backbone for both voice and data, carries both
T-1s operate over both copper and fiber.
Higher bandwidth than T-1 is fiber or digital radio only.
Notes: <number>

## Slide 17: Transmission: SONET (fiber)
Fiber bandwidth, beyond T-1
STS-1, or OC-1, is same as T-3, or 28 T-1s
SONET can be divided into channels as small as 64kbps
Voice carried at 64kbps or less (mobile as low as 9 kbps)
Data carried at many rates
Video carried at MPEG-1 (1.5Mb/sec) or MPEG-2 (6+Mb/sec); these are highly compressed
SONET superseded by OTN at 10 Mb/sec and above. More flexible frame, etc.
Mb/s
STS-768
STM-256
39.813.120
[TE] Chapter 5
Mb/s
Notes: <number>

## Slide 18: Exercise 4: Transmission
What is the bandwidth (digital) of an E1 channel? Ignore the framing bits. Give the result in both kbps and Mbps.
How many E1 channels can be carried in an STS-1 (or OC-1) channel?
  Round down by about 10% to allow for overhead.
  The result must be an integer.
How many voice calls (64 kbps) can be carried on the STS-1 channel over the E1s it contains?

## Slide 19: Solution
What is the bandwidth (digital) of an E1 channel? Ignore the framing bits.
  32 * 64 kbps= 2048 kbps, or 2.048 Mbps
How many E1 channels can be carried in an STS-1 (or OC-1) channel?
  Round down by about 10% to allow for overhead.
  The result must be an integer.
  Bandwidth after overhead= 0.9*51.84= 46.66 Mbps
  Channels= 46.66/2.048= 22+
  Round down to either 22 or 20.
How many voice calls (64 kbps) can be carried on the STS-1 channel over the E1s it contains?
  20 * 32= 640 (or 22 * 32= 704)

## Slide 20: Glossary
RFID: Radio frequency ID
SNR: Signal-to-noise ratio (decibels)
T-1: 1.5 Mbps transmission circuit (US)
E-1: 2 Mbps transmission circuit (Europe)
SONET: Synchronous optical network, fiber optic transmission standard
OTN: Optical Transport Network, for bandwidths beyond SONET using WDM (FDM)
MPEG-1, -2: Motion Picture Experts Group standards for video transmission, compression