## Slide 1: 1.264 Lecture 34
Telecom: Connecting wired LAN, WAN
Next class: Green chapter 17. Exercise due before class
http://web.mit.edu/subjectevaluation
Notes: <number>

## Slide 2: Exercise
Your transportation brokerage company also handles billing for freight shipments, collecting from shippers and forwarding payment to carriers.
  This data must be secure; you route funds directly to banks in some cases and between customers in other cases.
How would you communicate between your three major sites in New Jersey, Houston and Los Angeles?
  You transfer approximately 10,000 bills of lading in a 1 hour window at the end of each day from Houston and Los Angeles to New Jersey, which is the only site connected to banks and customers
  Each bill is about 500 kB of data (documents and signatures are scanned)
Select the technology and bandwidth
  Will you use LAN, WAN or MAN technology, or combination?
  Which specific technologies will you use? Discuss options, pros/cons briefly.
  Discuss broader options surrounding your choice.
Notes: <number>

## Slide 3: Solution
Bandwidth:
  500 kB x 8 bits/byte x 10 000 docs / 3600 seconds/hr
  Approximately 11 Mbps raw data rate
  Connection should be at least 15 Mbps, for overhead, etc.
  If we route LA traffic via Houston, Houston-NJ needs 25-30 Mbps
  Either case requires OC-1 (45-51 Mbps) bandwidth
Technology: WAN between LANs at each site
  With only two links (LA-Houston and Houston-NJ), two point to point fiber optic links are a possible solution
    Used only 1 hour a day, though…
  Internet could handle it but large bursty traffic across the country would have reliability problems
    Business traffic has security issues on open Internet
  Satellite bandwidth too low (network video has special deal).
Notes: <number>

## Slide 4: Solution, p.2
Business process can/must change:
  Established years ago with small amount of data and expensive telecom
  Cheaper to send documents in real time now
  If docs sent in real time 10 hrs/day, bandwidth = 1.5Mbps, which can be handled by T1, DSL, … much less expensively. 1.5 Mbps is a sweet spot.
  Or, look further: do we need to send all 500 kB to the bank? If we store the full document, can we send just the part the bank needs? Trade off complexity vs cost
Another reason why we use spiral model
  Telecom considerations at the very end can require changing a business process
    Which requires changing requirements among channel partners
    And changes UML, database (maybe), Web services, etc.
  If we find this in the first spiral, we can change it
  If we find this at the end of chaos/waterfall, it can be desperate
Notes: <number>

## Slide 5: LAN, WAN and access (last mile)
LAN
LAN
WAN/
MAN
Notes: <number>

## Slide 6: Outside plant
[TE] Chapter 7
Notes: <number>

## Slide 7: Feeder and distribution cable
Feeder cable becoming all-fiber. Some distribution is fiber, more planned
Notes: <number>

## Slide 8: Metropolitan area networks (MANs)
MAN is public network that bridges LAN and WAN, typically spanning 5 to 50 km
  Metro area Ethernet becoming dominant:
    Simple for customer, extends Ethernet LANs
    Carrier technology sophisticated but available, reliable, fairly low cost
  Runs over carrier fiber optic networks
  Shared across business users
    Security options: encryption or physical separation
  Not connected to open Internet or consumers
Applications
  Connecting LANs (sites) within a metro area
  Storage area networks (SANs)
  Connect many sites to one WAN point of presence (POP)
  Video, voice, graphics: bursty, high bandwidth data
Notes: <number>

## Slide 9: Metro area Ethernet
Gigabit Ethernet (1,000 Mbps)
  Compatible with Gigabit Ethernet LAN
  5 to 50 km range per hop
    Multiple Ethernet switches needed per metro area
  Available in many metro areas; can buy fractions of Gb
10G Ethernet (10 Gbps or 10,000 Mbps)
  Almost completely compatible with slower Ethernet
  Essentially compatible with SONET
    10G Ethernet is close to OC-192, and protocols map
  Range up to 40 km
  Becoming available; can buy fractions of bandwidth
Both options have technology (“tags”) to allow network to scale
    Ethernet switches discover all devices
    MAN Ethernet can have 100,000s of devices
Notes: <number>

## Slide 10: Access to metro area Ethernet
Ethernet in the First Mile (EFM)
  Copper: encapsulate Ethernet within modified DSL
    2 Mbps up to 2.7 km, 10 Mbps up to 0.8 km
  Fiber: essentially Gigabit Ethernet, up to 20 km
  Does not provide self-healing or diverse routing
Resilient Packet Ring (RPR)
  Provides alternate routes and failover, like SONET
    Dual counter-rotating rings
  Keeps Ethernet simplicity for applications, management
Notes: <number>

## Slide 11: MAN Ethernet
Notes: <number>

## Slide 12: Exercise: MAN
 | LAN | MAN
Distance (kilometers) |  | 
Owner |  | 
Number of devices |  | 
Bandwidth (Mbps) |  | 
Resiliency/redundancy (yes/no) |  | 
Is there a service level agreement (contract)? |  | 
Give approximate ranges for distance, devices, bandwidth.

## Slide 13: Solution
 | LAN | MAN
Distance (kilometers) | 1-5 km | 5-50 km
Owner | Company/user | Carrier
Number of devices | 10-1000 | 1000-100,000
Bandwidth (Mbps) | 100Mbps-1 Gbit/sec | 2 Mbps-10 Gbit/sec
Resiliency/redundancy (yes/no) | No | Yes, usually
Is there a service level agreement (contract)? | No | Yes

## Slide 14: Access technologies to connect LAN to WAN, if there is no MAN
Known as ‘last mile’ problem
  High bandwidth at LAN and MAN, but little in ‘last mile’
Digital subscriber line (DSL)
  Provided over existing copper lines to telco switch
  VZ (and others) moving DSL users to 4G LTE, in preparation of abandoning copper plant
Cable access
  Provided over existing coax cable to CATV head end
Wireless access
  4G cellular “long term evolution” (LTE)
  Satellite, in remote/ocean/air settings
Fiber to the business/home/curb
[TE] Chapter 8
Notes: <number>

## Slide 15: Digital Subscriber Line (DSL)
Many technical variations: ADSL, HDSL, SDSL, VDSL
Typically 12-18,000 foot limit; data rates of 500 kbps up to 8 Mbps
or carrier
Ethernet
Notes: <number>

## Slide 16: Asymmetric DSL (ADSL)
Copper line from customer to central office can handle 1.1 MHz, in theory
  Many impairments (noise, crosstalk, etc.) exist
Upstream ADSL uses 24 4.3kHz channels
  Almost same as voice channel, carries 60 kbps (not 64)
  In theory, we get 24 * 60 kbps, or 1.44 Mbps up
  In practice, we get 500 kbps
Downstream ADSL uses 224 4.3kHz channels
  In theory, we get 13.4 Mbps
  In practice, we get 8 Mbps or less
Other variations
  HDSL uses 2 pairs for 1.5 Mbps up to 12,000 ft
  SDSL uses 1 pair for 768 kbps up to 18,000 ft
  VDSL may get 3-25 Mbps over 3,000+ ft

## Slide 17: Cable access
Cable channel is 6MHz wide for broadcast video
  Cable bandwidth is 750 MHz approximately (coax)
  Downstream video: 45-550 MHz: 80 channels at 6 MHz
  Downstream data: 550-750 MHz: 33 channels at 6 MHz
  Upstream data: 5-42 MHz: 6 channels at 6 MHz
  Each channel can carry ~10 Mbps of data downstream, ~5-10 Mbps upstream
  Bandwidth shared across all cable users in segment
DOCSIS is cable standard for data
  Ethernet-like protocol. Users contend/collide to send.
  Data seen by all devices on cable segment, so it’s sometimes encrypted using RSA (public key encryption) and other protocols
Notes: <number>

## Slide 18: Cable TV
Often fiber now
Notes: <number>

## Slide 19: Wireless access
4G cellular data (“long term evolution”: LTE)
  20 Mbps, though bandwidth may saturate
  Replacing fiber to homes, small businesses
Satellite
  Downstream speeds acceptable (a few Mbps)
  Upstream links either not available or very expensive
    128-256kbps can cost $800-$1,000/month
    Satellites have limited power, long paths, high losses
    Satellite paths have high delays, unsuitable for interaction
  Can serve rural areas
We cover wireless in detail later
Notes: <number>

## Slide 20: Exercise
You have a depot in an industrial area without carrier fiber optics
You have 1,000 buses that return to the depot every evening and upload video to a remote site
Each bus has 10 hours of 384 kbps video.
Data goes via WiFi (wireless LAN) from each bus to a depot server, and then to the remote server.
You want all data to transmit in 2 hours.
Choose between DSL, cable TV and 4G wireless access. Which of these 3 can handle it?
  If they can’t, what do you need?

## Slide 21: Solution
Data/sec= 1,000 veh * 384 kbps= 384 Mbps
Time to send= 2 hr
Time to record= 10 hr
  Thus, the data must be sent 5 times as fast as it was recorded.
Bandwidth= 5 * 384 Mbps= 1920 Mbps= 1.92 Gbps
DSL, CATV or 4G/LTE cannot handle this
You need OC-48 (2.5 Gbps) over fiber to do this.
  You might be better off having each bus send real time video over LTE, though it would be expensive… You could sample, have driver control it (usually), etc.

## Slide 22: Glossary
ISP: Internet Service Provider
NAP: Network Access Point: ISP interconnect point
Feeder: Telecom cable from central office (CO) to service area interface (SAI) in neighborhood
Distribution: Telecom cable from SAI to end point
EFM: Ethernet in First Mile: access to MAN
RPR: Resilient Packet Ring: access to MAN
DSL: Digital Subscriber Line: Internet access over copper
DSLAM: DSL access multiplexer, at central office
LEC: Local exchange carrier (e.g., Verizion, AT&T)
DOCSIS: Cable TV data standard, Ethernet-like