## Slide 1: 1.264 Lecture 35
Telecom: Fiber optics
Next class: Green chapter 18-21. Exercise due before class
Course evaluation at http://web.mit.edu/subjectevaluation/
Notes: <number>

## Slide 2: T1
T1 is shorthand for 1.5 Mbps connection
T1 is the standard over copper
T1 is used as a shorthand for this data rate over any medium
More formally, we use DS-1 to designate 1.5 Mbps over fiber (or coax or …)
  And DS-0 to designate 64 kbps (a voice call)
  And DS-3 to designate a T-3, which is 28 T-1s, and which fits within the fiber standard OC-1 (51 Mbps)

## Slide 3: Optical networking exercise
Long spans possible
  0.2 db/km loss implies 1% of signal carries 100 km without amplification
    DB= 100 km * 0.2 db/km= 20 db
    Loss= 10 (DB/10) = 102 = 100
    Signal= 1/loss= 0.01
  400 km spans are common on land, longer undersea
Exercise:
  With 0.15 db/km loss, what is signal strength 200 km from origin?
Notes: <number>

## Slide 4: Optical networking solution
Long spans possible
  0.2 db/km loss implies 1% of signal carries 100 km without amplification
    DB= 100 km * 0.2 db/km= 20 db
    Loss= 10(DB/10)= 102= 100
    Signal= 1/loss= 0.01
  400 km spans common on land, longer undersea
Exercise solution:
  With 0.15 db/km loss, what is signal strength 200 km from origin?
  DB= 200 km * 0.15 db/km= 30 db
  Loss= 10DB/10= 103= 1000
  Signal= 1/loss= 0.001
Notes: <number>

## Slide 5: WAN: Optical networking hardware
Notes: <number>

## Slide 6: Optical networking terminals and muxes
Fiber optic terminals: convert optical/electrical
  Slow and expensive compared to all-optical switch/router
  Optical amplifiers now exist: fast, low power
  Amplifiers available for 5 Tbps (5000 Gbps) signals
Wavelength division multiplexing (WDM)
  We can send light of different colors in the same fiber to increase capacity
  Coarse WDM has 16 wavelengths
  Dense WDM has 40 wavelengths, going to 80-160
Notes: <number>

## Slide 7: Optical network operations
Common fiber operation in telecom trunks:
  OC-48 to OC-768 (2.5 to 40 Gb/sec) on a single pair of fibers
    Separate receive and transmit paths (no circuits)
    32,000 to 512,000 64kb/sec circuits for voice or data
    About 1,000 to 16,000 video channels at 1.5 Mbps
  Nationwide systems in US:
    Typically 48-fiber bundles over 25,000 mile network
    Several competing networks exist
  Diverse routing a problem for reliability (fiber cuts)
    Rights of way limited; multiple carriers hit by same outage
  Dark fiber becoming available for users
    Over metro area, can run corporate Ethernet to multiple sites
  Fiber to the premises (home, small business, …) available
    Verizon not building out home FIOS; business fiber continues
  Fiber used within corporate buildings and campuses
    Little fiber to desktop yet, but likely to come
Notes: <number>

## Slide 9: Exercise
Suppose 10 real time video channels (training, videoconference, customer contact…) are active in each of the 48 lower states in the US and made available to your company’s facilities in each state (You may be FedEx, UPS…)
  Real time channel is 6 Mbps
  Assume the location in each state uses every channel, so all 48 * 10 channels must be sent to each state
  All locations are in metro areas
How much bandwidth into each state is required?
  Can one 40 Gbps network handle it?
  If not, how many networks must be used?
Once the data gets to a metro area, can a 1 Gbps Carrier Ethernet handle all the traffic?

## Slide 10: Solution
48 states * 10 channels * 6 Mbps= 2880 Mbps= 2.88 Gbps
  One network can handle it, though it takes almost 10% of its capacity
  In a metro area, 1 Gbps is not enough. At least 3 1 GB networks are needed.
  This fills the entire capacity of these three networks. The carrier providing them must dedicate three sets of core and edge routers, plus spares.

## Slide 11: Optical network bandwidth
Fiber is faster than coax, copper or other electronics due to basic physics. Informally:
  There can be many bosons (e.g., photons) in one ‘place’ (quantum state) at the same time
  There can only be one fermion (e.g., electron) in one ‘place’ (quantum state) at the same time
This won’t change unless physics changes
  Fiber networks can haul 5,000,000 Mbps on a single wavelength on a single pair of fibers
    Fiber nets are often 48 pairs
    Dense wavelength division multiplexing can put 40-160 wavelengths on a fiber pair
  Wireless LANs (WiFi) can haul 30 Mbps (60% of 54 Mbps)
    4G metro wireless can haul 20 Mbps for a user
All other telecom technologies serve to provide access to fiber optic links. Fiber drives location for some industries.
Notes: <number>

## Slide 12
Or go to submarinecablemap.com
Notes: <number>

## Slide 13
Notes: <number>

## Slide 15
Notes: <number>

## Slide 16: African fiber links
afterfibre.net
Notes: <number>

## Slide 17: Exercise
A supplier is based in the interior of the Congo.
  It currently uses satellite communications at 128 kbps to access the Internet. It pays $500 per month per link.
  A fiber optic link becomes available that provides up to 45 Mbps, in 1.5 Mbps increments. The first 1.5 Mbps chunk costs $100 per month, and each increment costs $50
  It both sends and receives 100,000 XML messages per 8 hour day (orders, catalog, shipment, etc.). Half the messages are 10,000 bytes; the other half are 1 MB (with graphics)
  How many satellite links did it need, at what cost?
    If it needed more than 2, satellite was infeasible. It would have needed custom software to extract minimal data to/from XML messages handled by proxy elsewhere
  How much fiber bandwidth does it need, at what cost?
  What if it only sent and received 1,000 XML msgs per day?

## Slide 18: Solution
Bandwidth up= bandwidth down, as is common in business communications
  Bits/day= 50,000*8*(10,000 + 1,000,000)= 404 Gb
  Time= 8*3600= 28,800 seconds
  Bandwidth= 404 Gb/ 28800 sec=~ 14 Mb/sec
This is infeasible with satellites
  With 1,000 versus 100,000 messages, the bandwidth is 140 kb/sec. It would need 2 satellite links, at $1,000/mo.
With fiber this requires 15 Mb/sec at $100 + 9*$50, or $550 per month
  No proxy server or custom software are required, and the supplier is fully integrated via Internet/Web

## Slide 19: Technology comparison
Fiber optics (WAN)
  Bandwidth up to 5 Tbps (5000 Gbps) per fiber pair
  Number of fiber pairs unlimited
  Bit error rate: 10-14
  Distance spanned: 400 km between repeaters, global
Copper (existing telephone plant) (Access to WAN)
  Bandwidth up to 1.5 Mbps (T1) for long distances w/repeaters
    Up to 5 Mbps (DSL) up to 5 kilometers
    Up to 100 Mbps (LAN) up to 100 meters
  Bit error rate: 10-10
  Distance spanned: 2 km between repeaters, on land
CATV (coax) somewhat better than copper
Radio (microwave, mobile phone, wireless data) (WAN Access)
  Bandwidth up to~50 Mbps (microwave, WLAN), ~20 Mbps (mobile)
  Number of links limited by spectrum width (~5 GHz)
  Total wireless bandwidth ~ 10-15 Gbps at any point (2-3 bits/Hz)
  Bit error rate: 10-6
  Distance spanned: 100m (WLAN) to 20 km (microwave, mobile)
  Satellite has very high distance but same bandwidth, error rates
Error rates are critical; we’ll return to them
Notes: <number>