## Slide 1: 1.264 Lecture 33
Telecom: Wired LAN, WAN
Next class: Green chapter 8, 32. Exercise due before class
Notes: <number>

## Slide 2: Exercise
What’s on a telephone pole?
  Three types of network; name them
Which is highest on the pole? Why?
Which of these are point to point connections?
Which are shared (point to many)?
Which of these can carry data?
Which of these can carry voice?
Which have competitive (open) access?
What type(s) of wiring does each use?
Notes: <number>

## Slide 3: Solution
What’s on a telephone pole?
  Electric
  Phone
  Cable TV
Which is highest on pole? Why?
  Electric, high voltage/current
Which of these are point-to-point connections?
  Phone only
Which are shared (point-to-many)?
  Electric, cable
Which can carry data?
  Phone, cable, electric
Which can carry voice?
  Phone, cable, electric
Which have competitive access?
  Phone: unbundled to CLEC
  Cable: not competitive
  Electric: distribution monopoly, generation competitive
What type(s) of wiring does each use?
  Phone: copper, fiber
  Cable: coax, fiber
  Electric: copper
Notes: <number>

## Slide 4: Telecom systems management
Your project/system must estimate the amount of data to be exchanged with partners/servers
  Warehouse RFID example from last lecture
You must choose appropriate technologies
  Wired: higher bandwidth/reliability (~gigabits/sec/circuit)
  Wireless: mobile, flexible, low bandwidth (~megabits/sec/cell)
You must choose between build, lease, or service
  Depends on right of way, scale
You will interconnect different network types
  Local area (LAN), metro area (MAN), wide area (WAN)
Your networks will be standards based
You must choose carriers, bandwidths, service levels, costs, etc., similar to physical transport
  You are likely to need a lot of bandwidth

## Slide 5: Telecom bandwidth
Bandwidth is a key issue
  All data carried over analog (continuous) circuits at the physical level
  None were designed for data: telecom circuits for voice, broadcast and CATV for radio and TV
  All have been repurposed to carry data while retaining their historic physical structure ($$$ existing capital)
  Analog bandwidth measured in Hz: cycles/second
    Wireless communications can carry 2 bits/Hz in 5 GHz band
    Wired communications have vastly more bandwidth
    Formula for digital bandwidth based on signal/noise ratio
  These factors determine the building blocks you’ll use
    Most channels have more bandwidth than 1 user needs
    Multiple users are multiplexed (shared) on comm channels

## Slide 6: Telecom networks
Data travels over different network segments
  LAN at your site: cheap, high bandwidth (1 Gbps+)
  Connection from your site to local switch/cable headend:
    Copper: ~5 Mbps, cost variable
    CATV: ~20 Mbps, cost variable
    Fiber: essentially unlimited, cost variable
  Telecom or CATV network: fiber, high bandwidth, cheap
    Synchronous optical network (SONET) rings
    Very high availability (99.999%), recover from many faults
  Data circuits are permanent, unlike voice calls
    Data packet flow over the permanent network is variable
    Carrier IP networks handle most voice, data and video
    Large routers exist at carrier switch facilities for IP traffic
  Carrier networks are generally not encrypted; rely on physical security

## Slide 7: Review: Data communication protocols
[TE] Chapter 6
Notes: <number>

## Slide 8: Review: TCP/IP
[TE] Chapter 6
Notes: <number>

## Slide 9: LANs and WANs
And/or MAN if within a metro area
Notes: <number>

## Slide 10: Local area network (LAN)
High speed, privately owned, short range network
  IEEE 802.3 or Ethernet is nearly universal
  Speeds of 10Mbps to 1Gbps (1000Mbps)
  Limited range: building or campus (1-5 km typical length)
    No permission for right of way on streets
  Carriers can extend Ethernet over metro area using Carrier Ethernet, a metro-area network (MAN)
    The technology is not Ethernet per se, but it looks like and is managed like Ethernet from the customer’s point of view
    We cover MANs later.
Notes: <number>

## Slide 11: Repeater, bridge/hub, router, gateway at customer site
Notes: <number>

## Slide 12: Ethernet (initial wired, current wireless version)
Protocol is carrier sense multiple access/collision detection (CSMA/CD).
Earliest wired Ethernet used this protocol also, now superseded.
Min frame= 512 bits
If sender sends 512 bits and has heard no
jamming signal, it can continue w/o interruption.
Worst case is farthest station collides and sends
jam signal, which must reach sender before it
sends more than 512 bits.
Notes: <number>

## Slide 13: Exercise- Maximum traditional LAN length
Maximum LAN length: L= ct/2
Speed of signal: c (2 x 108 m/sec, 2/3 speed of light)
Ethernet speed: s (e.g., 108 bits/sec, or 100Mb/sec)
Slot time t: 512/s (min Ethernet frame size=512 bits)
Compute L for a 100 Mb/sec LAN (s)
Compute L for a 1 Gb/sec LAN (s)
You’ll see the 1 Gb/sec LAN isn’t feasible with traditional LAN. 1 Gb/sec LAN uses:
  Full duplex (two wires per station, one to send, one to receive)
  Switches only, no repeaters or bridges, and no collisions
  Fiber optics (often), with 500 to 5000 meter segments
  Distance limited by signal fading, etc. (more on this later)

## Slide 14: Solution
Maximum LAN length: L= ct/2
Speed of signal: c (2 x 108 m/sec, 2/3 speed of light)
Ethernet speed: s (e.g., 108 bits/sec, or 100Mb/sec)
Slot time t: 512/s (min Ethernet frame size=512 bits)
Compute L for a 100 Mb/sec LAN (s)
  L= (2x108 * 512/108)/2 = 512 meters= 0.5 km
Compute L for a 1 Gb/sec LAN (s)
    L= (2x108 * 512/109)/2 = 51.2 meters= 0.05 km
  Even though collisions are avoided in full duplex, switched LANs, signal attenuation and other losses are limiting
  LANs typically are 5 km or less

## Slide 15: WAN: Telecom carrier network facilities
Wide area networks (WANs)
Carried over same physical facilities as voice (next lecture)
  Local loop, local switch, tandem switch, trunk
Carried on permanent circuits of much higher bandwidth than for a single voice call; no switching
Protocols based on ISO 7-layer model
  Mostly HTTP (Web services), tcp, and ip
  Regulated by routers and data switches
Data sessions are highly variable compared to voice, e.g.,
  Web browsing
  Bank ATM machine
  Database backup
  LAN interconnection
Data addresses are Ethernet addresses or IP addresses
  Not phone numbers
Carrier data network speeds 56 kbps to 40 Gbps per circuit
Carrier voice network secure without encryption
[TE] Chapter 3
Notes: <number>

## Slide 16: Wide area networks (WANs)
Differences from metro-area (MAN) or local-area (LAN) net:
  Global in scope
  Usually provided by multiple carriers (one is lead)
Legacy WANs are present but usually not good choices for new data comm needs:
  Private (point to point) circuits: expensive
  Dialup circuits: low bandwidth
  Frame relay: still viable, being superseded by IP (cost, reach)
  Multidrop networks
    Used for bank ATMs, point-of-sale (POS) terminals, lottery terminals
    Now that banks, stores have general Internet access, encrypted ATM and POS traffic often goes over the general access
  Packet networks (X.25): expensive, limited bandwidth
  VSAT (satellite): widely dispersed, low bandwidth service
IP-based networks becoming dominant
  Typically over a business-only, carrier-provided infrastructure separate from the open Internet
Notes: <number>

## Slide 17: Carrier/public network: major components
(rare)
(rare)
[TE] Chapter 2
Router or IP-PBX
Copper, becoming fiber or wireless
Notes: <number>

## Slide 18: Telecom service areas
Notes: <number>

## Slide 19: SONET
SONET uses time division multiplexing (TDM)
  All clocks in the network sync to a master clock
  Multiplexer/demultiplexers start/end a SONET circuit
  Add/drop multiplexers insert/extract subset of signals
An OC-1 signal is 51.84 Mbits/sec
  A voice call is 64 kbits/sec, or 0.064 Mbits/sec
  Maximum capacity= 51.84/0.064, or 810 voice channels
  However it has about 15% overhead (framing, control)
  It actually carries 672 voice channels
  Or 7 to 28 video channels (1.5 Mbps to 6 Mbps)
An OC-192 signal is 192 times higher capacity
  Maximum SONET rate (though fiber can go higher)

## Slide 20: Fiber optic (SONET) rings
[TE] Chapter 5
Notes: <number>

## Slide 21: Exercise: SONET
You are a large airline with a single server site that handles all your reservations
  Average transaction is 10,000 bytes (80,000 bits)
  You must handle 2,000 transactions/second
Where can you locate your servers on the network in the previous slide:
  At central office A, in a telco colocation site?
  At a SONET hub on one of the OC-12 rings?
  At a multiplexer on one of the OC-3 rings?
Compute the server bandwidth and compare to the network bandwidth
  OC-3 is 3 * OC-1; OC-12 is 12 * OC-1; OC-48 is 48 * OC-1

## Slide 22: Solution
You need 80,000 * 2,000= 160 Mbits/sec
OC-1 is 51 Mbits/sec
OC-3 is 155 Mbits/sec. Not enough
OC-12 is 622 Mbits/sec. Clearly enough
You need to be at central office A or at a SONET hub on one of the OC-12 rings.
  You don’t need the full OC-12 or OC-48 capacity. Carriers will sell you an appropriate fraction.

## Slide 23: Glossary
Repeater: layer 1 LAN device
Bridge: layer 2 LAN device
Router: layer 3 LAN device
Gateway: layer 7 LAN device
VSAT: Very Small Aperture Terminal (satellite)
X.25: Packet service, pre-Internet (replaced by IP)
PBX: Private branch exchange, to switch voice calls in an office (now mostly IP-PBX)
LATA: Local access and transport area, defines service areas for regulatory, pricing issues