## Slide 1: 1.264 Lecture 37
Telecom: Enterprise networks, VPN
Notes: <number>

## Slide 2: Enterprise networks
Connections within enterprise
External connections
  Remote offices
  Employees
  Customers
  Business partners, supply chain partners
  Patients…and other actors with special requirements
Principles of enterprise network design
  Standards based
  Secure
  Reliable: disruptions affect all external connections
  Quality of service: latency, throughput, services, …
Notes: <number>

## Slide 3: Building blocks of enterprise network
Local area networks
Wide- or metro-area networks: include 1 or more of:
  Private lines (point to point circuits)
  “Carrier Ethernet” MAN over carrier fiber in metro areas
  Virtual private net (VPN) over Internet
  Private or carrier-provided networks separate from Internet
    Frame relay (pre-Internet, still used but being superseded)
    Label switched (MPLS), over carrier IP network
    Covered later in this lecture
Voice network: includes one or more of:
  Integrated with data network
  Private lines shared between data and voice
  Voice carried over IP or MPLS network
Video network
  Usually carried as service over data network
Notes: <number>

## Slide 4: Virtual private networks (VPN)
Notes: <number>

## Slide 5: Virtual private networks (VPNs)
Definition: VPN is set of sites that
  Communicate over the open Internet but
  With the security and management capabilities of dedicated circuit or frame relay network
  Supporting applications without modification
  With simple management for admins and users
  And with low overhead and good communications performance
  Typically handle data only but can handle voice, video
VPN basic functions
  Authentication (identity), authorization (privileges)
  Establishment of secure tunnel (path) in network
Notes: <number>

## Slide 6: VPN technology
VPN tunnel encapsulates data of one protocol inside the data field of another protocol
  VPN encrypts corporate data inside IP packet data field (which is managed by TCP, which is called by HTTP)
    HTTP and TCP data is inside the IP packet and is encrypted
  The corporate data is encrypted via the VPN’s security protocol (symmetric, asymmetric keys, message digests)
    SSL is frequently used; Kerberos-like options also available
VPNs operate at layer 2 (Ethernet) or layer 3 (IP)
  Layer 3: Routers use IP information to route
    Most common: Easier to manage, but lower performance
  Layer 2: uses Ethernet addresses; corporation responsible for routing packets across WAN and LANs
    Harder to manage, but better performance
VPNs operate over DSL, cable, etc.
  Simple network topology (all links to/thru central point)
  Limited redundancy, resiliency
Notes: <number>

## Slide 7: VPN tunnel
Internet carries packet between routers R1 and R2
Packet is encrypted, and intruder only sees R1 and R2 IP addresses
Actual IP addresses (100 and 200) cannot be seen, nor the packet contents

## Slide 8: VPN terminology
Intranet
  Portion of VPN connecting internal sites
Extranet
  Portion of VPN connecting external sites
Security protocols
  Secure Sockets Layer (SSL)
  IPsec (secure IP standard) at layer 3
    Can encrypt entire packet (tunnel mode) or just the data field (transport mode)
    All devices must share a common (public) key, in digital certificate
    Devices negotiate secure tunnel using Internet Key Exchange (IKE) protocol
  Layer 2 tunneling protocol (L2TP)
    Requires pre-arranged paths between devices or to/from secure server
Notes: <number>

## Slide 9: Enterprise routing: IP and other protocols
Notes: <number>

## Slide 10: Multiprotocol Label Switching (MPLS)
Label edge routers (LERs) assign a label that defines the path the packet will take through the IP network
  Routing happens only once, at edge
  Routing at interior routers (label switched routers, or LSRs) is done in hardware, not a software lookup of IP routing tables
    Much faster, cheaper
    A stack of labels allows complex, hierarchical networks
  Label distribution protocol (LDP) used to distribute labels to all LSRs and LERs, using TCP/IP
  MPLS allows QoS, security (strict traffic rules)
    MPLS VPNs operate at layer 2 or layer 3
    Corporate routers don’t need to support MPLS; they connect to LER via IP
  MPLS is a fiber-only technology, national but not global scope (yet), complex network, “Ethernet-like” operation
Notes: <number>

## Slide 11: Multiprotocol Label Switching
Network neutrality debate…
Notes: <number>

## Slide 12: Virtual LANs
MPLS is sometimes described as implementing a virtual LAN, or VLAN: set up LANs in software
Source: Forouzan

## Slide 13: Technology changes
Next slide compares X.25 and frame relay
  X.25 was developed for copper or radio long-haul networks with high error rates
  Link-by-link error correction as a message travels across the network
  Assumes ‘dumb’ equipment at the edges, so the X.25 protocol takes full responsibility for delivering messages correctly
Frame relay (or any other protocol carried on fiber optics such as TCP/IP)
  Relies on low fiber optic error rate. No link-by-link error correction, just a retransmission triggered by end node if message not correctly received
A wireless long haul net would need roughly the same protocols as X.25
  Smart edge devices make it easier than X.25
Notes: <number>

## Slide 14: Frame relay vs X.25
Notes: <number>

## Slide 15: Frame relay/Internet vs. X.25
Difference between reliable and unreliable networks
  Fiber has error rate of 1 bit in 1014; can correct end-to-end
  Wireless has error rate of 1 bit in 106; must correct link-by-link
Difference between smart and dumb terminals
  Formerly, terminals had no CPU and just displayed what the communications line sent to them
    Could not detect or correct errors
  PCs, servers, smart phones as terminals can correct and detect errors
“Hollowing out of the network”
  Network (switches, etc.) used to have all the intelligence
  Now network is just a set of ‘bit pipes’
  Edge devices have the intelligence
Notes: <number>

## Slide 16: Telecom convergence
Convergence: Moving all voice, data and video traffic onto Internet
  Consumer service reasons:
    Smart cards and mobile phones: browsers, phone as payment medium, smart posters, cameras
    E-commerce generally
  End of the personal computer (PC) as we know it, for most users
  Cost reduction: one network versus many
    Private nets morph into carrier nets with Internet protocols
  Increased mobility services
    Tying wireless access to fiber optic backbone flexibly
  Barriers:
    Low quality, chaos of open Internet to reach customers
    Security to reach customers
    Broadband in the ‘last mile’ to reach businesses and homes
Notes: <number>

## Slide 17: Glossary
VPN: Virtual private network
IPsec: Secure IP (layer 3 security used in VPNs)
L2TP: Layer 2 tunneling protocol (VPN)
PSTN: Public switched telephone network, or carrier network
MPLS: Multiprotocol Label Switching, a WAN technology to connect LANs transparently
  LER: MPLS Label Edge Router
  LSR: MPLS Label Switched Router (interior)
  LDP: MPLS Label Distribution Protocol
QoS: Quality of service

## Slide 18: Steps and skills for building these systems are same as we’ve covered in class this semester
Software engineering and project management
  People, process, product, technology dimensions
  Select development method (often spiral model)
  Requirements, design, resource estimation, implementation, QA
Process modeling
  UML: describe use cases, states, activities, classes, components
  Used in requirements, scoping, design early; architecture late
Data modeling
  Model business rules, verify with users (internal, customers, …)
  Normalization, referential integrity
Database
  Relational databases, SQL at core of applications, Web
  Databases read/write XML
Notes: <number>

## Slide 19: Steps, continued
World Wide Web:
  Connect clients and servers: HTTP, XML, Web services
  Use HTTP, XML as universal data access
  XML allows human, machine and document interpretation
  XML documents include business rules, database schema
Security
  Protocols codify rules, principals, risks, …
  TLS and Kerberos
  TLS encryption, certificates, digital signatures
  People, process, product, technology dimensions again
Networks
  Multi tier : Web, application, database
  7 layer data comm model: HTTP (7), TCP/IP (4/3), Ethernet (2)
  LANs, MANs, WANs: LANs, MANs are Ethernet, WANs vary
  Fiber optic core, wireless/copper/CATV for access
  Use private/carrier network, not open Internet in many cases
Notes: <number>

## Slide 20: Course summary: process
If you spent 12 hours per week for 14 weeks, that's 168 hours, or 4 40 hour weeks
Ready for second spiral after 8 person weeks of work (4 person weeks times 2 people)
  This can be done in the wasted “up-front” time to prepare for an anticipated project
  It will usually take this long because you'll usually be learning a new domain and/or new technology
By using the spiral model and being able to do requirements, UML, data models, SQL, Web sites, initial security approach and initial telecom approach, you can:
  Work effectively with IT staff
  Manage engineering or logistics projects with IT components
By knowing technical areas covered in class, you can:
  Specify, design and build databases, Web sites, etc. as a consultant
Notes: <number>